## Slide 1: Open Discussion
Re: Future Internet Protocol Evolution and Ways Forward
Questions to and Discussion with the Community

## Slide 2: Engagements since FIPE @ IETF108 Move possibly to opening discussion
Drafts proposed to community
  FlexIP in IntArea
  Stewart & Toerless draft fill in
  COIN RG draft on micro-services
Engagements with research community
  Richard? Toerless?…
Liaised with other efforts
  ITU FG Network2030, 6G Networking Whitepaper @ 6G Flagship, …
Feedback from partners
  Narrow discussions to concrete research problems -> FIPE @ IETF109

## Slide 3: R & long-term-D areas for future network protocols
Multi-semantic addressing/routing
Energy & packet-size efficient steering
Variable length addressing
Beyond single global address space
Hierarchical & multi-layer semantics
FreeChoice/Unified: IPv4/v6+Ethernet+MPS+future
Geo-addressing (e.g.: satellites)
ManyNet partial connectivity addressing
(beyond NAT, ULA)
On-demand capabilities & guarantees
Beyond 8-Bit TOS services headers
Better explicit ECN/PCN/CC signaling (e.g. beyond L4S)
Up-speeding signaling
Differentiated fair bandwidth (e.g.: NADA, DPS)
Loss management (e.g.: PEROF beyond MPLS)
Latency signaling/services beyond deterministic (e.g.: LBF)
SLO vs SLA signaling (throughput, loss, latency)
Monitoring / Accounting signaling
Hop-by-hop packet programmable headers– efficient, scaleable (low..high speed) unified:
Enabler & Dependency for any new addressing/routing and capabilities/guarantees!
Beyond P4 (Data-Center) variable length field programmable processing engines
Programmable QoS (e.g.: PIFO, PIEO, LBF)
Context: Future Use-cases and Networks (not current networks / hardware)
use-cases eg: FGNET2030, Networks: Future Metro, Satellite, Many-Nets (Industrial/Vertical), 6G
Industry,
Other SDO

## Slide 4: Candidate Semantic Addressing Research Questions
What types of innovation would be unleashed by unshackling the address semantics?
Is this a path that allows networks to become as programmable as applications?
What other functions (beside steering, destination) can we map to address?
What other types of cardinality are useful?
Do the same considerations apply to the underlay, overlay and the end-user application?
How do we achieve aggregability of addressing with opaque addresses?
What would be its implications, from efficient hardware support to late binding of semantics?

## Slide 5: Candidate capabilities and guarantees Research Questions
Can we provide better differentiated capabilities and guarantees in a scalable, fashion (e.g. without per-flow state and upfront admission control)
Can we improve fundamentally on mixing different service traffic without class-based managed resource division (e.g.: beyond PI^2 / L4S, for e.g. slices)
What is the most lightweight/scalable option to provide ”sufficient” stochastical guarantees ?
Can we eliminate complexity of layered inconsistent service differentiation across multiple layers (Ethernet + MPLS + IP) ?
What service value can we achieve from signaling SLO and SLA in packets ?
What value can we get from explicit signaling of latency for packets ?
What service aspects can help monetization of service differentiation ?

## Slide 6: Packet programmability research questions
How do network programming models need to evolve to allow network providers to develop new networking services?
What would be the impact on network APIs, socket interfaces etc – how would they change, what would be effective ways of giving providers control?
What are implications on efficient hardware support, enabling to run commands/instructions at line rate?
What ways are there to exploit parallelism and the ability to process different commands / parts of the packet concurrently? How do packets need to be designed / encoded to facilitate that? Where do non-blocking extensions make sense (e.g., to separate updates to OAM data from packet forwarding)
What are proper security models for packet-programmable networks
How is proof-of-processing supplied, how are incentives to honor SLO/SLA/contracts given?
What are efficient ways to secure and tamper-proof packet metadata and incremental / aggregated operations across a path – lightweight authentication, fine-grained authorization with low packet and processing overhead
Algorithms for packet/flow programming: how can applications take advantage of this
Algorithms for assurance: smart telemetry, aggregation of OAM data, enhanced diagnostics, etc
Algorithms for service level guarantees: service-level aware fowarding/QoS, etc.

## Slide 7: Future Internet Protocol Evolution FIPE positioned originally as an INITIAL FORUM to study that evolution
Initially - dedicated RG !?
  Inclusive like 1990’th IPNG-WG, but research question oriented & Research Coordination ?
Evolve into separate RGs for specific areas? (addressing vs. Services ?)
Evolve into engineering aspects (packetization ?) Experimental IETF WG ?
How to interact with community for other relevant work in IETF/IRTF?
TSV-WG
RMCAT-WG
DETNET-WG
COIN-RG
ICC-RG
6MAN-WG
PAN-RG
MPLS-WG
IPPM-WG
SPRING-WG
OTHER-WG
Scatter topics across wide number of existing RG/WG ?
What is the right forum to discuss the long-term evolution of IP in these key areas?
Difficult to separate common packetization vs. multiple services achievable through new packet formats!

## Slide 8: Old Slides

## Slide 9: FIPE @ IETF109
Research questions on multi-semantic addressing & routing and provisioning of on-demand capabilities with guarantees for network
Do the research questions warrant work in the IRTF or IETF?
If not, where else?
  Already done in IETF/IRTF?
  Research outside IRTF?
If yes, where?
  IETF (existing or new WG) and/or IRTF (existing or new RG)

## Slide 10: Future Internet Protocol Evolution FIPE positioned originally as a forum to study that evolution
What is the right forum to discuss the long-term evolution of IP in key areas?
Dedicated RG?
Several RGs for specific areas?
How to interact with community in terms of other relevant work in IETF/IRTF?