## Slide 1: Candidate FIPE research questions / areas
Toerless eckert (tte@cs.fau.de) Futurewei, USA
Alexander Clemm (alex@futurewei.com), Futurewei USA
Stewart Bryant (sb@stewartbryant.com), Futurewei USA

## Slide 2: Changelog
Not yet capturing all the side meeting outcomes, but hopefully good starting point
See the other repositories under github.com/network2030 for those and other work.

## Slide 3: Desired goals / benefit
Review & Renew IETF fundamental network layer research / experimentation
  After 30 years, A new round of IP-NG (early 90th)
    SRv6, 17++ IPv4/IPv6 transition solutions show limits of IPv6/RFC8200. IETF work is small & incremental only
  No forum for researchers to get together and collaborate on fundamental network layer research
    Everyone is in their silo, at best few region (USA, Europe, China) funded for limited collaboration
  And IEEE 802.x eats IETF protocols lunch
    IP replaced more and more by L2 switching
    Better in QoS support (.e.g.: TSN,…) , fast adopting IETF technologies (SPB),
    Vice versa not (DetNet still on basic MPLS data plane only), only rehashing IEEE technologies
Hop-by-hop network layer work extremely fragmented across groups in IETF/IRTF:
  ICNRG (mostly tactical to support QUIC), PANRG (mostly tactical on path telemetry to support SDN), COIN (all-inclusive charter, but predominantly focussed on higher layer functions, not network layer hop-by-hop functions),
  6MAN (maintainer of the IPv6 status quo: RFC8200/IPv6 base header is holy grail), MPLS (life support), SPRING (deadlocked arguing limited alernatives to SRv6), TSVWG (Mostly maintenance of legacy, e.g.: one new DiffServ code point every few years), ...

## Slide 4: Areas of interest
“High Precision Communications” (HPC)
    TOS/DiffServ: 6 bit Class QoS from 1981/199x / IntServ
    Research
      Need to research how to bring better, more scalable, more valuable hop-by-hop traffic service management into network
      We call this “High Precision Communications QoS” (HPC)
    Short term experimentation opportunities:
      Replace / amend base IP headers for e.: DetNet / Scaleable DetNet (today only MPLS headers defined)
Network Packet header encoding research (“progammable packets”)
    Candidate goals: “Generic forwarding protocol” , reuseable across layers
Addressing: Variable length / multi-semantic “FreeChoice” / hierarchical
    Candidate goals: IPv6 backward compatible Future IP that also works better for controlled / non-Internet networks, can support also deployments where Ethernet or MPLS are preferred/better today (e.g.: integrate with those protocol services)
Many dependencies between these three areas. Initially better to start with a shared group
  “lighthouse” / “dispatch” group etc.
  Could equally be IRTF RG or Experimental IETF WG – practical experimentation very much desired!
    Experimental IETF WG would invite more experimenters in our opinion

## Slide 5: High Precision Communication services
Beyond 8 bit „QoS“ in packets: what could/should services be: existing / new research how would/could it be expressed in network header:
Congestion Control (CC)
  ECN vs. PCN - currently use same bits to signal, but deliver different experience.
  More than 2 ECN bits for faster CC level signaling (LIVE research paper)
  Upspeeding indication (minimum free path bandwidth ?!)
Throughput
  Explicit signaling associated with difference in target bandwdidth e.g.: as possible in NADA (weight)
  signaling of flow-bandwidth for stateless weighted fair queeuing (DPS research 2010)
Loss
  Signaling of discard priority (known benefits for video, e.g.: I/P/B differentiation – payloadencr ypted.
  Signaling of flow copy MRT/Live-Live high-resilience deployments. sub-flow ?
  Sequence number (as required by PEROF DetNet, not existing for IP)
Latency
  latency SLO , end-to end min/max, experienced latency, (see NOMS LBF paper)
  signaling of experienced latency for better per-hopp-functions
  discard packets early when they are too late (not based on hops)

## Slide 6: Wolpertinger One protocol to replace them all
“Common packet chassis” (like in todays car manufacturing)
  Can we create a seamless superset of MPLS, IPv4/v6, Ethernet, ..
  Without creating a “committee design”
  But make packet header the programmable network language ?
Example approach: BPP
  Alex: research publications
  Various “researchy”?! ideas done / TBD:
    Actions, parameters, metadata, explicit paralelization/serialization,..
Overcome extensibility challenges of RFC8200
  Attribution, PMTUD, overhead
Invent once, reuse across existing network forwarding planes
  Avoid duplication as DetNet would be bound to do re. TSN (No IP support)
  HPC “QoS” inclusive of DetNet reuirements
Supporting variable length addresses / stacks prerequisite

## Slide 7: Packet programmability research questions (Alex)
How do network programming models need to evolve to allow network providers to develop new networking services?
What would be the impact on network APIs, socket interfaces etc – how would they change, what would be effective ways of giving providers control?
What would SDKs for such services look like, including sandboxes, test environments, and roll-out?
What are implications on efficient hardware support, enabling to run commands/instructions at line rate?
What ways are there to exploit parallelism and the ability to process different commands / parts of the packet concurrently? How do packets need to be designed / encoded to facilitate that? Where do non-blocking extensions make sense (e.g., to separate updates to OAM data from packet forwarding)
What are proper security models for packet-programmable networks
How is proof-of-processing supplied, how are incentives to honor “contracts” given?
What are efficient ways to secure and tamper-proof packet metadata and incremental / aggregated operations across a path – lightweight authentication, fine-grained authorization with low packet and processing overhead
Algorithms for packet/flow programming: how can applications take advantage of this
Algorithms for assurance: smart telemetry, aggregation of OAM data, enhanced diagnostics, etc
Algorithms for service level guarantees: service-level aware fowarding/QoS, etc.
Algorithms for other areas: security, etc

## Slide 8: Addressing Research Questions (Stewart)
What types of innovation would be unleashed by unshackling the address semantics?
Is this a path that allows networks to become as programmable as applications?
What other functions can we map to address?
What other types of cardinality are useful?
Do the same considerations apply to the underlay, overlay and the end-user application?
How do we achieve aggregability of addressing with opaque addresses?
What would be its implications, from efficient hardware support to late binding of semantics?

## Slide 9: Research & forwarding plane protocols
Interest in research community in a next-gen research forwarding plane protocol
  Vehicle for innovation
  Get research closer to high speed hardware (could also include ICN)
  Would well align with ongoing research interest in evolving programming language concepts (P4) and QoS concepts (PIFO, PIEO,…)
More inspiring ideas ? Object oriented packets ?
  How could we use object-oriented packets? What ramifications would they have on existing forwarding planes?
  What accessors need to be defined as part of OO packets? What types of methods should user be able to define? What abstractions are needed?
  How do network programming models need to evolve to allow network providers to develop new networking services?
  What would be the impact on network APIs, socket interfaces etc – how would they change, what would be effective ways of giving providers control?
  What would SDKs for such services look like, including sandboxes, test environments, and roll-out?
  What are implications on efficient hardware support, enabling to run commands/instructions at line rate?
E.g.: BPP and commands/contracts/metadata as a starting point idea ?

## Slide 10: References
See other papers in github.com/network2030/BPP

## Slide 11: Backup Slides

## Slide 12: FIPE questions from Huawei
https://github.com/FIPE-Study/Draft-charter/issues/1
Objectives
  To understand, document, and survey the scenarios, use cases and requirements that motivate the evolution of the Internet Protocol for various digital networked industries and societies. Potential scenarios include, but are not limited to, cloud computing, 5G/6G, space-terrestrial communication, and holographic communication, developing economies, disaster recovery, and etc.
  To discuss, assess, research and document technologies for specific use cases with a focus on the deployment issues such as compatibility, scalability, security, manageability, and interoperability.
  To discuss, assess, research and document the research on the principles and foundations of the future-oriented Internet Protocol designs that would suit future Internet and future applications.
Research Scope
  The scope of the FIPE Research Group includes study of enriched use cases and requirements as driven by the development of various digital networked industries and societies. Following our motivation above, our research as follows will revisit the principles and foundations of the Internet Protocol design for fundamental improvements.